## Slide 1
Chapter 02
Calibre nmDRC Basics
Set up runs · Review results · Work with RVE
Using Calibre nmDRC/nmLVS • Chapter 02

## Slide 2
Chapter Overview
PART 01
Set Up an nmDRC Run
Specify rule files
Specify input & output info
Specify nmDRC options
Execute the job
PART 02
DRC Output Results
Review run transcript
Review DRC Summary Report
View results in RVE
PART 03
Common DRC RVE Tasks
Modify check/cell tree display
Cross-probe to layout viewer
Manage result status & waivers

## Slide 3
nmDRC Layout Verification Process Flow
Layout
(.gds file)
Rule File
(.rules)
Calibre nmDRC
DRC Report
(optional)
DRC Results
Database
Locate errors
(RVE + Layout tool)
Fix Layout
Errors
Notes: This is the core iterative loop: layout + rules → nmDRC engine → results → fix → repeat until zero violations.

## Slide 4
PART 01
Set Up an nmDRC Run

## Slide 5
Part 1 — Objectives
By the end of Part 1 you will be able to:
Specify rule files — point Calibre to the foundry's design rule file
Specify input information — provide the layout file and top cell name
Specify output information — set results database and summary report paths
Specify nmDRC job options — configure parameters like maximum results per check
Execute the nmDRC job — run from the GUI or command line

## Slide 6
Executing a Calibre nmDRC Job
1
Specify Rule File
Point to the foundry .rules file
2
Specify Input Info
Layout file path + top cell name
3
Specify Output Info
Results DB + Summary report paths
4
Specify nmDRC Options
e.g. max results per rule check
5
Execute nmDRC Job
Click Run DRC or run from terminal
GUI Method: Calibre Interactive — fill in forms, Calibre generates SVRF automatically. | Command Line: Write settings in a SVRF runset file, invoke calibre from the terminal. Both methods are equivalent.

## Slide 7
Step 1 — Specify the Rule File
In the Calibre Interactive GUI:
Click Rules in the left navigation panel
Type the rule file name in Rules File (e.g. drc.rules) or browse to it
Click Load — populates other GUI fields from the rule file
Optionally click View to inspect the rule file contents
Equivalent SVRF command:
INCLUDE "drc.rules"
💡 Key Insight
The GUI "Rules File" field is a visual wrapper around the INCLUDE statement. Typing drc.rules in the GUI and clicking Run DRC causes Calibre to generate INCLUDE "drc.rules" internally.
// Job and User settings SVRF file
LAYOUT PRIMARY lab1 // TOPCELL
LAYOUT SYSTEM GDSII // file format
LAYOUT PATH "/home/student/work/lab1.gds"
DRC RESULTS DATABASE lab1.drc.results ASCII
DRC SUMMARY REPORT lab1.drc.summary
INCLUDE "drc.rules" ← THIS step
INCLUDE "golden_rules"

## Slide 8
Step 2 — Specify Input Information
In the Calibre Interactive GUI:
Click Inputs in the left navigation panel
Set Layout Format — almost always GDSII
Set Layout File — path to your .gds file (e.g. lab1.gds)
Set Top Cell — name of the top-level cell (e.g. lab1)
Enable Export from layout viewer to automatically stream the latest layout from your editor
What is a Top Cell?
IC layouts are hierarchical — like a tree. The Top Cell is the root. Calibre starts there and traverses all subcells. Always match the name exactly as it appears in your .gds file.
Equivalent SVRF commands:
LAYOUT PRIMARY lab1
LAYOUT SYSTEM GDSII
LAYOUT PATH "/home/student/work/lab1.gds"
LAYOUT PRIMARY lab1 // ← top cell
LAYOUT SYSTEM GDSII // ← format
LAYOUT PATH "..." // ← THIS step
DRC RESULTS DATABASE lab1.drc.results ASCII
INCLUDE "drc.rules"

## Slide 9
Step 3 — Specify Output Information
A) DRC Results Database
Primary output — contains all violations with exact coordinates
Format: ASCII (human-readable) or binary
File: e.g. lab1.drc.results
B) DRC Summary Report (optional)
Enable: check DRC Summary Report in Outputs pane
File: e.g. lab1.drc.summary
Set Previous contents to REPLACE to overwrite each run
Optionally auto-open after run finishes
Option | What it does
Output cell errors in cell space | Report errors in the cell's own coordinate system (recommended)
Side RDBs | Create extra results databases for specific checks
Create HTML Report | Generate a web-browser-friendly version of results
DRC RESULTS DATABASE lab1.drc.results ASCII // ← THIS step
DRC SUMMARY REPORT lab1.drc.summary // ← THIS step

## Slide 10
Step 4 — Specify nmDRC Options
Accessing Options in the GUI:
Settings → Show Pages → Options (makes Options visible)
Click Options in the left navigation panel
Select the desired tab inside the Options pane
Set values and click Run DRC
Example — DRC Maximum Results
Limits how many violations are stored per rule check. Default = 1000.
Why? If a systematic error causes 500,000 violations of the same rule, storing all of them wastes disk space. 1000 representative examples are enough to find and fix the root cause.
DRC MAXIMUM RESULTS 1000
⚠️ Not all SVRF options are available in the GUI. If you cannot find an option in the Options pane, consult the SVRF Reference Manual and add it directly to your runset file.

## Slide 11
Step 5 — Include Another SVRF File
Why include multiple rule files?
Foundries often split rules across multiple files — a main drc.rules file plus supplemental golden_rules files. You can include as many as needed; they are processed in order, top to bottom.
In the GUI — Options pane:
Open the Options pane
Scroll to Include Rules Files and check the checkbox ✓
Type the additional file name (e.g. golden_rules) or browse to it
Equivalent SVRF command:
INCLUDE "golden_rules"
INCLUDE "drc.rules"
INCLUDE "golden_rules" // ← THIS step
DRC MAXIMUM RESULTS 1000

## Slide 12
Step 6 — Execute the nmDRC Job
Click Run DRC
at the bottom of the left panel in Calibre Interactive.
Or from command line:
calibre -drc -hier my_runset.svrf
What happens after clicking Run DRC:
Transcript pane opens and shows the live run log
Summary line appears when complete: 0 Errors, 1 Warning, 1 Info
Results database is written to the path you specified
Summary report opens automatically (if enabled)
Key statistics at end of transcript:
--- TOTAL RULECHECKS EXECUTED = 11
--- TOTAL RESULTS GENERATED = 57 (230)
--- DRC RESULTS DATABASE FILE = lab1.drc.results (ASCII)
Field | Meaning
TOTAL RULECHECKS EXECUTED | Number of individual rules checked
RESULTS GENERATED = 57 (230) | 57 stored; 230 actual count before the limit
DRC RESULTS DATABASE FILE | Confirms output file path and format

## Slide 13
PART 02
DRC Output Results

## Slide 14
Part 2 — Objectives
After the job finishes, there are three output review tasks:
Task | Tool | What you learn
Review the Transcript | Terminal or GUI Transcript pane | Execution details, warnings, timing, expansion info
Review DRC Summary Report | Text editor or GUI Files pane | Which rules were checked and how many violations each has
View results in RVE | Calibre RVE | Interactive graphical error browser with layout cross-probing

## Slide 15
Review the Transcript
Two places to read the transcript:
Command line run → prints to the terminal window
GUI run → appears in the scrollable Transcript pane inside Calibre Interactive
Both show identical content
What to search for:
ERROR or WARNING — find problems quickly
RuleCheck COMPLETED — see result counts per check
EXPANDING — identify expanded (flattened) cells
TOTAL RESULTS GENERATED — end-of-run summary
Layer active_CO::<1> DELETED -- LVHEAP = 1/3/4
DRC RuleCheck active_CO COMPLETED. Number of Results = 21
--- TOTAL RULECHECKS EXECUTED = 2
--- TOTAL RESULTS GENERATED = 23 (23)
--- DRC RESULTS DATABASE FILE = demo_drc.db (ASCII)
--- CALIBRE::DRC-H COMPLETED -- Wed Jan 19 13:04:20 2022
--- PROCESSOR COUNT = 1

## Slide 16
Review the DRC Summary Report
1. Job Information
Execution date/time, Calibre version, rule file name, layout path, top cell, max results, output file paths
2. Runtime Warnings
Any warnings generated during the run (e.g. memory tuning suggestions)
3. Layers Processed
Each input layer and the number of geometric shapes found on it
4. RuleCheck Statistics
How many violations each rule check found, broken down by cell — the most important section
RULECHECK active_CO ..... TOTAL Result Count = 21 (21)
RULECHECK poly_CO ....... TOTAL Result Count = 2 (2)
CELL TOP ... TOTAL Result Count = 23 (23)
RULECHECK active_CO ... TOTAL Result Count = 23 (23)
RULECHECK poly_CO ..... TOTAL Result Count = 2 (2)

## Slide 17
Invoke RVE to View DRC Results
From command line:
grep "DRC RESULTS" demo.rules
# DRC RESULTS DATABASE demo_drc.db
calibre -rve demo_drc.db
From Calibre Interactive GUI:
Run Control pane → RVE Options
✅ Show Results in RVE
✅ Start RVE as soon as results are available
RVE Interface — Key Panels:
Panel | What it shows
Check / Cell Summary Tree | All rule checks and cells with violations
Results List (top right) | Numbered list of violations for selected check
Results Details (bottom right) | Geometric coordinates of selected violation
Rule Check Comments (bottom bar) | Author's notes explaining the check

## Slide 18
PART 03
Common DRC RVE Tasks

## Slide 19
Modify RVE Check/Cell Tree Display
Go to: View → Tree Options → Group By
Group By Option | Tree Structure | Best Used When...
Check / Cell (default) | Rule checks → expand to see cells | Fixing one rule at a time across all cells
Cell / Check | Cells → expand to see failed checks | Fixing all issues inside one cell at a time
Check | Rule checks only — no cell breakdown | Quick count of violations per rule
Cell | Cells only — no check breakdown | Quick count of violations per cell
Cell / Check view example:
✗ Cell lab2 Results: 4
✗ Check min_spacing_metal1 3
✗ Check min_spacing_metal2 1
✗ Cell a2311 Results: 3
✗ Cell a1230 Results: 1
Sorting & Other Options
Click any column heading to sort by that column — sort Results ↓ to see worst offenders first
Show Empty Checks — display checks with zero violations
Show Branch Prefix — show full hierarchical cell path

## Slide 20
Cross-Probe DRC Results to Layout Viewer
Step-by-step cross-probing:
Select a rule check from the Check / Cell tree that has errors (e.g. Check active_CO)
Click the highlight icon in the RVE toolbar and choose a highlighting mode
Double-click an error number in the Results List — the layout viewer instantly zooms to that location and highlights the violation in red
Read the Rule Check Comments at the bottom of RVE — the rule author explains what is being checked and often gives fix hints
Highlighting Option | Effect
No View Change | Highlight but do not move the layout view
Pan to Highlights | Pan layout view to show the error
Zoom to Highlights ★ | Zoom in to the error — RECOMMENDED
Clear Existing Highlights | Remove all current highlights
💡 Workflow Tip
Use 'Zoom to Highlights' as your default. After fixing an error in the layout editor, come back to RVE, right-click the error, and mark it Fixed to track your progress.

## Slide 21
Displaying Errors in a Hierarchical Design
Setting | Error coordinates in RVE | Layout viewer behavior
Cell space OFF | Top cell coordinate system | Error marker appears in top-level view — may need to zoom in
Cell space ON ✅ (default) | Local cell coordinate system | RVE opens the cell and zooms directly to the error inside it
Enable in GUI — Outputs pane:
Outputs pane → check ✅ Output cell errors in cell space
This is the DEFAULT setting in the Calibre Interactive GUI. It is the recommended setting for all hierarchical designs.
⚠️ What If Error Is Still at Top Level?
Calibre may expand (flatten) certain cells internally for performance. When a cell is expanded, its violations are reported at the parent level, not inside the cell.
Check the Transcript for EXPANDING lines to see if your cell was flattened:
a1720 in lab1 at (308.25, 355) ← expanded!

## Slide 22
Set DRC Result Display Format
Click the icon in the upper right of the Results List to switch display mode:
List View
1 2 3
Plain numbered list. Compact, good for many results.
Icons View
✗1 ✗2 ✗3
Numbers with status icons showing fix/waive state.
Details View
ID | Flat | #EC | #EL | #EW | Vertices
1 | 1 | 4.0 | 4.9 | 0.2 | 4
Full table with ID, coordinates, vertex count. Best for geometric analysis.
💡 The toolbar icon updates to reflect the currently selected mode. The Details view column #EC = error x-centroid, #EL = y-centroid, #EW = error width.

## Slide 23
Set DRC Result Status
✗
Not Fixed
Default. Violation has not been addressed. Appears in red.
✓
Fixed
Layout has been edited to correct this violation. Appears in green.
◌
Waived
Violation intentionally accepted (pre-approved exception). Appears dimmed/gray.
How to set status:
Right-click one or more results in the Results List
Choose Fix, Waive → Waive, or turn both off to return to Not Fixed
Important behaviors:
Waived results persist — saved to <result_file>.waived, survives between runs
Fixed results reset — cleared on each re-run (correct: must re-run to confirm the fix worked)

## Slide 24
Comment and View Waived Results
Enable waiver comments:
Click the Setup gear icon in the RVE toolbar
Go to the Waivers category
Check "Show comment dialog while waiving results"
Click Apply
Waived Result Comment
Waived by student on Thu Jun 01 08:24:17 PDT 2017
─────────────────────────────────────
This error waived per Ted Smith.
─────────────────────────────────────
[ OK ] [ Cancel ]
Three ways to view waiver comments:
1
Hover tooltip
Hover the mouse over a waived result (dimmed X) in the Results List. A tooltip pops up showing the comment text.
2
Open .waived file in RVE
File → Open Text File → select <result>.waived. Shows all waived errors with coordinates and comments.
3
Create ASCII Waiver Report
Tools → Create Waiver Report → save as .txt. Generates a clean summary for design review packages and tapeout checklists.

## Slide 25
Chapter Summary
Concept | Key Takeaway
nmDRC Process Flow | Layout + Rule File → nmDRC engine → Results DB → RVE → Fix → repeat
Two run methods | GUI (interactive) and SVRF runset file (command line / automation)
INCLUDE | SVRF command to load a rule file into the job
LAYOUT PRIMARY / SYSTEM / PATH | Set top cell name, file format, and layout file path
DRC RESULTS DATABASE | Set output results file name and format (ASCII or binary)
DRC SUMMARY REPORT | Set the optional human-readable text summary file name
DRC MAXIMUM RESULTS | Limit violations stored per rule check (default 1000)
Transcript | Real-time run log — check for EXPANDING, warnings, result counts
DRC Summary Report | Post-run overview — best place to see which rules failed and how many
RVE | Graphical error browser with layout cross-probing
Cell space errors | Errors in local cell coordinates — default, recommended for hierarchical designs
Result Status | Not Fixed (red) / Fixed (green) / Waived (gray); waived results saved to .waived file

## Slide 26
Quick Reference — Job Settings SVRF File
// ============================================================
// Job and User settings SVRF file
// Most basic setup file for DRC and LVS run
// Date: 12/1/2021
// ============================================================
// --- INPUT SETTINGS ---
LAYOUT PRIMARY lab1 // Top cell name in the layout
LAYOUT SYSTEM GDSII // Layout file format
LAYOUT PATH "/home/student/work/lab1.gds" // Path to layout
// --- OUTPUT SETTINGS ---
DRC RESULTS DATABASE lab1.drc.results ASCII // Violation data
DRC SUMMARY REPORT lab1.drc.summary // Text summary
// --- OPTIONS ---
DRC MAXIMUM RESULTS 1000 // Max violations per rule check
// --- RULE FILES ---
INCLUDE "drc.rules" // Main foundry rule file
INCLUDE "golden_rules" // Additional rule file
💡 Save this as a template. Change only the layout path, top cell name, and output file names for each new project.