## Slide 1
Chapter 10
Electrical Rule Checks
& Antenna Rule Basics
Using Calibre nmDRC/nmLVS
SIEMENS

## Slide 2
Objectives
1
Learn antenna theory basics — what causes the antenna effect and why it matters
2
Use Calibre to identify antenna problems using NET AREA RATIO rules
3
Perform ERC (Electrical Rule Checks) during an LVS run
4
Generate geometric output files (GDSII/OASIS) from a Calibre nmDRC run

## Slide 3
Electrical Rule Checks (ERC)
Questions ERC Can Answer
Which nets have a path to ground (including through devices)?
Which nets do NOT have a path to power or ground?
Which PMOS devices are connected to VCC through PSD?
Why ERC Requires LVS
Needs connectivity extraction
Must know which shapes form which nets
Traces through devices
Must follow nets through transistors & resistors
Runs inside LVS job
LVS already extracts connectivity — ERC reuses it
ERC ≠ DRC: ERC asks "Is my circuit connected correctly?" — not just "Do my shapes follow geometric rules?"

## Slide 4
Calibre ERC Operations
PATHCHK
Reports nets in the layout that do, or do not, have a path to power, ground, or labeled nets — or any combination of these conditions.
DEVICE LAYER
Derives a layer containing all device seed shapes from all device instances of a named type (e.g., all NMOS gate shapes).
Key SVRF Statements
ERC RESULTS DATABASE
result_file // File where ERC results are written
ERC SELECT CHECK
rule_check ... // Which ERC checks to execute
ERC SUMMARY REPORT
report_file // Human-readable run summary (optional)
ERC results are viewed using RVE — exactly like DRC results.

## Slide 5
ERC Workflow — 6 Steps
1
Specify Output Info
ERC RESULTS DATABASE result_file
2
Enable Checks
ERC SELECT CHECK rule_name
3
Disable Checks
ERC UNSELECT CHECK rule_name
4
Limit Result Count
ERC MAXIMUM RESULTS 50
5
Execute the Job
calibre -spice … -hier rule_file
6
View in RVE
Open ERC Results tab in RVE

## Slide 6
ERC: Output Info & Check Selection
Step 1 — Specify Output
ERC RESULTS DATABASE
lab5a.erc.results
ERC SUMMARY REPORT
lab5a.erc.summary
LVS EXECUTE ERC
YES
ERC SUMMARY REPORT is optional but recommended.
Steps 2 & 3 — Select / Unselect Checks
// Enable a check:
ERC SELECT CHECK
erc_rule_metal1_no_power
// Disable a check:
ERC UNSELECT CHECK
erc_rule_metal2_no_power
By default: NO checks are executed in LVS.
ERC SELECT CHECK builds the list; UNSELECT removes from it.
Step 4 — Limit Result Count
ERC MAXIMUM RESULTS
50 // Stops writing after 50 results per check. Default = 1000

## Slide 7
Execute the ERC Job & View Results
Step 5 — Execute
// Command line:
calibre -spice "alu.sp" \
-hier my_rules
// Or with explicit LVS flag:
calibre -spice … -lvs … rule
LVS EXECUTE ERC YES
ERC runs during LVS extraction phase.
"LVS EXECUTE ERC YES" is optional — ERC runs by default once checks are selected.
Step 6 — View in RVE
🔍
ERC Results tab
Lists checks with violation counts
📄
ERC Summary tab
Full run log with layer statistics
📌
Layout highlight
Click result → highlights shapes in viewer

## Slide 8
Generating Geometric Output From Calibre
You can instruct Calibre to write DRC results to a GDSII or OASIS file using DRC CHECK MAP:
DRC CHECK MAP
rule_check [GDSII|OASIS] layer datatype filename
Example 1: Grow metal1 by 0.1u and save as GDS
Grow_Metal1
{@ SIZE metal1 BY 0.1 }
DRC CHECK MAP
Grow_Metal1 GDSII 21 0 "./mask/grown_m1.gds"
Example 2: Output all metal shapes on net "RESET" as GDS
LAYER m_123
metal1 metal2 metal3 // Define combined layer set
Plot_RESET
{@ NET m_123 RESET }
DRC CHECK MAP
Plot_RESET GDSII 1 0 "./plots/RESET.gds"

## Slide 9
What Is an Antenna?
How the Antenna Effect Happens
1
Charge builds up
During plasma etching, metal/poly interconnect paths collect electrical charge — acting like antennas.
2
Charge seeks ground
Large charge accumulations find a path to ground through the gate region.
3
Gate oxide damaged
Charge arcs from poly through the thin gate oxide to the well — destroying the transistor gate permanently.
Antenna Effect — Schematic View
antenna (long metal wire)
well
⚡ gate destroyed!
⚠️ Cannot be repaired after fabrication.
Antenna violations = dead chips = yield loss.
Must be caught before tape-out!

## Slide 10
Antenna Rule Basics & Net Area Ratio (NAR)
Net Area Ratio (NAR)
NAR =
Antenna Area
Gate Area
A large NAR → more charge risk → higher damage probability
Antenna rules flag nets where NAR exceeds the foundry limit.
SVRF Syntax
NET AREA RATIO
metal1 metal2 poly
gate
> 20
RDB
"antenna.rdb"
metal1 metal2 poly
antenna_layers — interconnect layers that accumulate charge (metal1, metal2, poly)
gate_layer — the layer defining gate area (the denominator)
ratio_limit — foundry-specified maximum allowed NAR (e.g., 20)
RDB keyword — outputs ALL listed layers to the results DB, not just the first

## Slide 11
Additional Antenna Considerations
As interconnect layers are added during fabrication, antenna nets grow and gate areas change:
Add metal1
⬛⬛⬛
3 antennas, 2 gates each
MET1a, MET1b, MET1c are separate nets — each connects to only 2 gates.
Add metal2
⬛⬛
2 antennas: 1×2 gates, 1×4 gates
Metal2 bridges some segments together, merging nets. Gate count changes.
Add metal3
⬛
1 antenna, 6 gates
Metal3 connects all segments into a single net spanning all 6 gates.
Key insight: Adding metal layers can REDUCE antenna violations by merging small antenna nets (with few gates) into larger shared nets (with more gates) — changing the NAR.

## Slide 12
Chapter 10 — Summary
ERC
Electrical Rule Checks — answer connectivity questions; require LVS
PATHCHK
ERC operation: reports nets with/without path to power/ground
DEVICE LAYER
ERC operation: derives a layer of device seed shapes by type
ERC RESULTS DATABASE
Specifies where ERC results are written
ERC SELECT CHECK
Enables specific checks for ERC execution (none run by default)
ERC UNSELECT CHECK
Removes checks from the execution list
ERC MAXIMUM RESULTS
Caps results per check (default = 1000)
Antenna effect
Charge buildup on interconnect during fabrication damages gates
NAR
Net Area Ratio = antenna area / gate area — key antenna metric
NET AREA RATIO
SVRF operator that computes NAR and flags violations
DRC CHECK MAP
Writes rule check results to GDSII or OASIS geometry files
SIEMENS · Using Calibre nmDRC/nmLVS · Chapter 10